## Slide 1: Cinterion IoT Embedded Processing
Nov 2021

## Slide 2: Cinterion Embedded Processing Evolution
2005
2006
2007
2008
2009
2010
2011
2012
2013
2014
2003
2004
2015
2016
2017
2018
2019
2020
2021
2022
Phase 3
Efficient, resource optimized platforms
Phase 2
First IoT focused Platforms
Phase 1
Feature Phone Platforms
TC65
EGS5/TC65i
TC65i-X/EGS5-X
TC45
EHS5
EHS6
EHS8, PDS5
ELS6
PLS..
EXS..
TX..
Notes: Key messages:
Our 20 yrs experience and evolution of products with EP, and now we arrives at a phase of EP on optimized platform, where:
Efficient embedded systems
Best leverage of system resources
Highly integrated applications
Tying in sensors and other peripherals

## Slide 3: Cinterion Embedded Processing & its SDK
  The Thales IoT SDK makes module’s onboard resources available for the application:
  Processing
  Memory
  Interfaces
  GNSS
  Security
  The Thales IoT SDK ties all these resources into a secure and flexible development environment, for easy and fast IoT application creation.
Modem
GNSS
Processor
Security
Interfaces
Memory
IoT Application
Cinterion IoT
Embedded Processing
Efficient Focused System
EMBEDDED PROCESSING
SDK
Efficient embedded systems
Best leverage of system resources
Highly integrated applications
Tying in sensors and other peripherals
Notes: Cinterion EP allows the Customers’ application to be placed inside the module itself, and allows application to access/use the module on-board resources, such as its memory, GNSS, interfaces and security.
Thales also provide a unique SDK to develop the application.

## Slide 4: Main Elements for Embedded Processing
Security
Cinterion IoT SDK for Embedded Processing
Easy and flexible way to build a complete IoT Application
Cinterion IoT Embedded Processing
Leveraging Thales IoT Module onboard resources
Cinterion IoT Suite
IoT Application update over-the-air*
* in future releases
Notes: Thales EP has 3 main elements: EP itself, SDK and IoT Suite to do the OTA application update, encapsulated by Thales security framework

## Slide 5: General Advantages for Embedded Processing
  Improve BOM costs
    Remove cost for processor and memory
    No software license costs for OS and development tools
  Process improvements
    Simplified supply chain with less components and supplier dependencies
  Build minimal space applications
    Remove Processor space
    Remove Memory space
    Simpler power supply
  Fast prototype and design
    No extra hardware development for processing
    Proven ready to go package
    Leverage pre-integrated IoT building blocks
    Maximize software reuse with industry standard software and tools
Reduce Total Cost of Ownership
Optimize the Application
Shorten Time-To-Market
Notes: With semicond supply issues nowadays, the role of EP has become more and more visible and critical
In the next slides, my colleague Jacques will present ‘why Thales SDK?’, what are the differences vs other module vendors?

## Slide 6: Solution Technical Overview
Application Core
  Cortex A7 @ 800MHz, 1520 DMIPS
  The application core is running
    Thread-X Operating System
    Thales Service APIs: a set of IoT middleware libraries
    OEM app
Typical OEM app Memory Profile (on EXS-TX)
  Code: 512 KB
  Volatile Data: 256 KB
  Non Volatile Data (File System): 512 KB
OEM app has a direct access to hardware peripherals from application core
UART
SPI
I2C
GPIO
EXT_IT
USB
ADC
Application Core
Cortex A7
@800MHz
Modem Core
QDSP6
@576MHz
SIM
RF
GNSS
FLASH
64 MB
RAM
32 MB
PCM/I2S
shared memories

## Slide 7: Supported Use Case
Cooperative Mode
A external MCU driving the module through AT commands is offloading code inside the module
Standalone Mode
The complete OEM application is hosted inside the module
AT cmd
AT cmd
Custom Modem
The OEM is extending the list of AT commands supported to resell a custom terminal (or module)

## Slide 8: RunTime Architecture
Application binary
Cortex A7
ADC
EXT_IT
GPIO
I2C
SPI
UART
USB
Socket
(UDP, TCP, PING, IP v4, IP v6)
Secure Socket
(TLS, DTLS)
File System
GNSS
Power Mgmt
Thread-X
OEM Application
Network
Control
Thales Services & Thread-X
OEM app
OS & Drivers
Service APIs
Serial Port
Safe Update
AT Client
Watchdog
App Logging
HTTP(S)
MQTT
NIDD

## Slide 9: SDK Service APIs
Thales is exposing following Service APIs for OEM app
  Thread-X RTOS API
    For Operating System interface: ThreadX User Guide
  Qualcomm QAPI
    For hardware peripherals (I2C, ADC...)
    For Sockets, IP protocols & File System
    For modem functionalities
  Thales GINA Service API
    Unified serial interfaces (for any UART or USB-CDC ACM)
    Safety procedures for software update
    Application management (watchdog, cleanup) and logs
    Security services

## Slide 10: SDK Tools
USB
UART
I2C
GPIO
EXT_IT
ADC
SPI
Command line tools for an easy integration with Continuous Integration
  Usable from Windows and Linux host
  Target connection primarily through USB
  Tools for
    Building the OEM app inc. toolchain and cross compiler
    Downloading the OEM app into the module
    Configuring & getting logs from the OEM app
      Through dedicated serial port (any physical UART or logical USB port)
      Through URC multiplexed into an AT channel
    Exploring the application core File System

## Slide 11: SDK Service APIs – GINA Application Management
Watchdog Reset
  System reset if your application falls into infinite loop
Resource cleanup
  Callback to properly release your resources in case of application stop/update
Custom Update procedure
  Update firmware or application
  Either locally (e.g. UART) or remotely (e.g. HTTP)

## Slide 12: SDK – Errors & Exceptions Management
Backtrace
  Get the last called functions before a crash
Exception Handler
  Catch exceptions for unauthorized memory or resource access
  Configure behavior depending on error type
    Ignore
    Restart app
    Restart app wo. data re-initialization
    Stop & unload app
user@host:~$ python backtrace.py process exception3 1 ..\examples\exception3 .
Process Dump 1 of APP exception3...
Received 100 %
sp is 0x43004c78, stackStart is 0x43003d30
lr is 0x43000254
pc is 0x430001e8
*** Exception occurred at PC 0x430001e8 in function Func3 at line #139
in exception3.c
*** Called from 0x43000250 in function Func2 at line #154 in exception3.c
*** Called from 0x43000278 in function Func1 at line #162 in exception3.c
*** Called from 0x430002f8 in function _APP_main at line #184 in exception3.c
LR 0x0 - end of call stack detected

## Slide 13: SDK – Secure your application
Application Signing
  Prevent malware injection
  Using your own key pair
  PuK/certificates stored in Thales certificate store
Reduce interfaces & commands
  Locking peripheral interfaces (UART, SPI, …)
  Locking commands on AT Interfaces
  Locking File System rights & access
  Locking Userware app & logs
Certificate Store
IoT Application
Firmware
eFUSE

## Slide 14: Cinterion Embedded Processing Products
2021 H2
2021 H2
2021 H1
Phase 3
Efficient, resource optimized platforms
PLS..
EXS..
TX..
EXS62 / EXS82
TX62 / TX82
PLS63 / PLS83
IoT Application
Cinterion IoT
Embedded Processing
IoT Application
Cinterion IoT
Embedded Processing
IoT Application
Cinterion IoT
Embedded Processing

## Slide 15: Customers

## Slide 16: Tracesafe LTE-M Gateway – Singapore (ASEAN)
Thales IoT Embedded Processing and its SDK are easy to use, and have saved us efforts and bill of material cost by eliminating the need for an additional MCU in our design
-Jasling Ong (Managing Director of Tracesafe Asia Pacific)
Company: | TraceSafe
Country: | Singapore
Product name: | LTE-M Gateway
Module: | EXS82-W
https://www.tracesafe.io/
Gateways are the glue that holds the TraceSafe wearable ecosystem together. Placed strategically around your location, they extract real-time information and upload it to the cloud securely.
Product description:
Connects Bluetooth Low Energy (BLE) devices to LTE-M network
Built-in internal antenna, with an unobstructed range of 14 meters / 15 yards
61.7mm x 61.7mm x 2mm

## Slide 17
Thales and V2COM Partnership
Thales Embedded Processor is key for our products both on EHS6 with our Java powered application that can solve our complex business processes and EXS82 where our ConeraTM Middleware process the data to provide edge intelligence and better uses the Cellular LPWA connectivity
Thales SDK as well is deeply important as allow V2COM to abstract operations that would require effort of coding and testing, allowing V2COM team to focus on business application needs and reuse basic modules.
Frederico Vieira
Technology Development Manager
Água | Agronegócio | Energia | Indústria 4.0 | Petróleo e Gás | Smart City
EHS6
EXS82/62
NIC NT1050X
Motelight MTL31
NG2
GT650
GTPhases